## Slide 1: Lesson 6 – ROS - Assignment 1 Creating a 2D Map of an Unknown Environment by tutulebot3
Intelligent Mobile Robotics
Dr. Aboozar Taherkhani (PhD)
email: aboozar.taherkhani@dmu.ac.uk

## Slide 2: Overview
Visualising a grid map using rviz
Create a package contain python code to create a map
Use the odometry data in ‘/odom’ topic to find the position and orientation of the robot, i.e. (, , )
Use the sensor reading from ‘scan’ topic to find the position of an obstacle
Find the corresponding cell on the grid map to update

## Slide 3: Visualising a grid map using rviz
Rviz, abbreviation for ROS visualization, is a powerful 3D visualization tool for ROS

## Slide 4: Create an empty package called ‘mapping’

## Slide 5: ‘Mapper()’ class will create a map from laser scan data
Subscribes to ‘scan’ topic
its call back function is ‘self.scan_callback’

## Slide 6: ‘Mapper()’ class has a call back function: ‘self.scan_callback’
You could write your code in this function to plot on the map shown in rviz
Adjust the values of the grid cells, self._map.grid[i, j], and see what will happen on rviz

## Slide 7: Creating a map
Use the odometry data in ‘/odom’ topic to find the position and orientation of the robot in a 2D global coordinate system, i.e. (, , )
Use the sensor reading from ‘scan’ topic to find the position of an obstacle, i.e. (, )
Find the corresponding cell on the grid related to each obstacle, and change the probability of the cell on the grid map corresponding to the obstacle to 1

## Slide 8
(, , )

## Slide 9: 1-Use the odometry data in ‘/odom’ topic to find: (, , )
Subscribe to the ‘/odom’ topic
sub = rospy.Subscriber ('/odom', Odometry, get_rotation)
msg.pose.pose.position->(, )
msg.pose.pose.orientation->

## Slide 10: 2-Use ‘scan’ topic to find the position of an obstacle: (, )
Subscribe to the ‘scan’ topic
sub = rospy.Subscriber('/scan', LaserScan, callback)
Use ‘msg.ranges[0]’ to read the range (distance) of a barrier which is in 0 degree
So you have the direction, 0 degree, and the distance of the barrier, i.e. (r,)

## Slide 12: Use ‘scan’ topic to find the position of an obstacle: (, )
Subscribe to the ‘scan’ topic
sub = rospy.Subscriber('/scan', LaserScan, callback)
Use ‘msg.ranges[0]’ to read the range (distance) of a barrier which is in 0 degree
So you have the direction, 0 degree, and the distance of the barrier, i.e. (r,)
Find the local position of the barrier at (r,), i.e. (, ), using the trigonometry
Map the local coordinate of the barrier, i.e. (, ), to the global coordinate system using rotation and translation

## Slide 13
Please see the lab sheet for Lesson 6 on LZ to work on this week practical