## Slide 1: Lesson 5 Occupancy Grids (1) Probabilistic Modelling of a Sonar Sensor
AI for Mobile Robots:
Intelligent Mobile Robotics
Dr. Aboozar Taherkhani (PhD)
email: aboozar.taherkhani@dmu.ac.uk

## Slide 2: Overview
The occupancy grid
Modeling a sonar sensor
Maths
Implementation details

## Slide 3: The Occupancy Grid
The scattergram in the previous lesson is binary:
  A point in space is either occupied or not
Range readings are determenestics
However there are uncertainties:
  Wind
  Humidity
  Obstacle material properties
Occupancy grids attempt to mitigate some of these uncertainities

## Slide 4: The Occupancy Grid
Divide mapping area into a grid

## Slide 5: The Occupancy Grid
Grid size is proportional to computational complexity:
  How big is the area you are working in?
    5m X 5m
  Let a grid square cover 5cm X 5cm area
    100 x 100 squares
    10000 squares

## Slide 6: The Occupancy Grid
So each grid square represents an area of some size
Each square is assigned a probability
This is the probability that the square is occupied
  0 = definitely not occupied (white)
  1 = definitely occupied (black)
  0.5 = Equal chance of being occupied or unoccupied (grey)
All squares are initialised to 0.5

## Slide 7: The Occupancy Grid
Initial occupancy grid

## Slide 8: The Occupancy Grid
But how do we update it?
Sonar reading

## Slide 9: Sonar Model
Why do we need a sonar model?
  Readings are inaccurate
  Say we get a reading at (22.2,43.2) at a heading 70
  A probabilistic model of the sonar allows us to model the inaccuracies
  We can ask the questions like:
    Given the reading, what is the probability that there is an obstacle at (21.2,42.1)?
General question:
  Given the potential for uncertainty in the sonar reading at P what do I know about Q?

## Slide 10: Sonar Model
P
Q

## Slide 11: Sonar Model
We need a model of a sonar sensor
But what should its properties be?

## Slide 12: Sonar Model
We need a model of a sonar sensor
But what should its properties be?
Region 1
  The area immediately around the sonar reading
  Grid squares in this area have a probability of 1
To mark the obstacle taking into account:
  Uncertainty in the distance reading
  Uncertainty in angle

## Slide 13: Sonar Model
Simplest model
1
3
2

## Slide 14: Sonar Model
The area in between the sonar and obstacle should be free of obstacles
Grid squares in this area have a probability of 0
This is region 2
The area in on the other side of obstacle we have no knowledge of
Grid squares in this area have a probability of 0.5
This is region 3

## Slide 15: Sonar Model
Simplest model
1
3
2

## Slide 16: Sonar Model
Simplest model
1
3
2

## Slide 17: Sonar Model
Simplest model
P
Dist
1
0
1
3
2

## Slide 18: Sonar Model
Improving this model
1
3
2
Tend to 0.5
Tend to 0.5

## Slide 19: Sonar Model
More complex model
P
Dist
1
0
1
3
2

## Slide 20: Sonar Model
Some useful functions

## Slide 21: Sonar Model
Some useful functions

## Slide 22: Sonar Model
Some useful functions
a
b
c
d

## Slide 23: Sonar Model
Some useful functions
a
b
c

## Slide 24: Sonar Model
Some useful functions
y
x
x
y
(xn-1,yn-1)
(xn,yn)

## Slide 25: Sonar Model
Example from Murphy page 379

## Slide 26: Sonar Model
Example from me

## Slide 27: Sonar Model
How to get create a model like this?
  Use parametric functions
    Bell curve
    Triangle
    Trapezoid
  Parameters
    Angle
    Distance
  Combine these functions and plot in polar space

## Slide 28: Sonar Model
Example using linear interpolation
  Use two linear functions of distance for m and e
  Interpolate across these for angle
3000mm
β
d
m
e
e
β

## Slide 29: Sonar Model
Function m
Points = {(0,0),(max(0,d-150),0.25), (d,1.0), (min(d+150,3000),0.5), (3000,0.5)}
P
Dist
1
0
d
3000
150
0.25
0.5

## Slide 30: Sonar Model
Function e
Points = {(0,0.4),(max(0,d-150),0.5), (d,0.6), (min(d+150,3000),0.5), (3000,0.5)}
P
Dist
1
0
d
3000
0.4
0.6

## Slide 31: In Cartesian Co-ord Space