## Slide 1: Lesson 9– Path planning
Intelligent Mobile Robotics
Dr. Aboozar Taherkhani (PhD)
email: aboozar.taherkhani@dmu.ac.uk

## Slide 2: Pathplanning
Different path Planning algorithms:
  Graph based
  Topological
  G.A.
They all need some form of configuration space or CSpace

## Slide 3: Pathplanning
A mapped environment:

## Slide 4: C Space
A grid:

## Slide 5: C Space
A meadow map:
  A number of convex polygon (interior angle is less than 180o )

## Slide 6: C Space
A generalised Voronoi graph:

## Slide 7: C Space
A Relational Model (landmarks and gateways):
landmarks
gateways

## Slide 8: Grid Based Pathplanning
A* (or D*) path planning

## Slide 9: Grid Based Pathplanning
Easy to construct
Lets look at A*

## Slide 10: A* Search
Variant of best first
Guaranteed to find the shortest path when:
  The quality measure works on partial paths
  The newest node is added to the head of the list and the list is reordered

## Slide 11: A*
Start in the red node
Goal is the green node
Blue nodes are walls
Number of nodes = w X h
Open and closed list of nodes
Each node is given an F,G and H score

## Slide 12: A*
Scoring the node:
  G Score
    Think of geographical score
    The distance it has taken to get from the starting node to the current node
  H Score
    Think of heuristic score
    The estimated distance from the current node to the goal node
    We’ll use Euclidean distance
  F Score
    Think of final score
    F = G + H

## Slide 13: A* Pseudo Code
create the open list of nodes, initially containing only our starting node
create the closed list of nodes, initially empty
while (we have not reached our goal) {
consider the best node in the open list (the node with the lowest f value)
if (this node is the goal) {
then we're done
}
else {
move the current node to the closed list and consider all of its neighbours
for (each neighbour) {
if (this neighbour is in the closed list and our current g value is lower) {
update the neighbour with the new, lower, g value
change the neighbour's parent to our current node
}
else if (this neighbour is in the open list and our current g value is lower) {
update the neighbour with the new, lower, g value
change the neighbour's parent to our current node
}
else this neighbour is not in either the open or closed list {
add the neighbour to the open list and set its g value
}
}
}
}

## Slide 14: A* (A star)
Run until goal node is found
Reconstruct path using record of parent nodes

## Slide 15: A* (A star)
Run until goal node is found
Reconstruct path using record of parent nodes
A* pathplaning: https://www.youtube.com/watch?v=-L-WgKMFuhE

## Slide 16: Wavefront Path planning
BFS (Breadth First Search) alternative to A*
BFS search from goal to start node
Only based on geographical score
Move to the (unvisited) adjacent node with the lowest score
If you have a choice, take the node which requires the least turning

## Slide 17: Wavefront Pathplanning
BFS path planning
 | 15 |  |  |  |  |  |  |  |  |  | 
 | 14 | 14 |  |  |  |  |  |  | 6 |  | 
 | 13 | 13 |  |  |  |  |  |  | 5 | 5 | 
 | 12 | 12 |  |  |  |  |  |  | 4 | 4 | 
 | 12 | 11 |  |  |  |  |  |  | 3 | 3 | 
 |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 
 |  |  |  |  |  |  |  |  |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 0 | 
Goal
Start

## Slide 18: Wavefront Pathplanning
BFSpathplanning
 | 15 |  |  |  |  |  |  |  |  |  | 
 | 14 | 14 |  |  |  |  |  |  | 6 |  | 
 | 13 | 13 |  |  |  |  |  |  | 5 | 5 | 
 | 12 | 12 |  |  |  |  |  |  | 4 | 4 | 
 | 12 | 11 |  |  |  |  |  |  | 3 | 3 | 
 |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 
 |  |  |  |  |  |  |  |  |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 0 | 

## Slide 19: Wavefront Pathplanning
BFSpathplanning
 | 15 |  |  |  |  |  |  |  |  |  | 
 | 14 | 14 |  |  |  |  |  |  | 6 |  | 
 | 13 | 13 |  |  |  |  |  |  | 5 | 5 | 
 | 12 | 12 |  |  |  |  |  |  | 4 | 4 | 
 | 12 | 11 |  |  |  |  |  |  | 3 | 3 | 
 |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 
 |  |  |  |  |  |  |  |  |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 0 | 

## Slide 20: Wavefront Pathplanning
BFS path planning
 | 15 |  |  |  |  |  |  |  |  |  | 
 | 14 | 14 |  |  |  |  |  |  | 6 |  | 
 | 13 | 13 |  |  |  |  |  |  | 5 | 5 | 
 | 12 | 12 |  |  |  |  |  |  | 4 | 4 | 
 | 12 | 11 |  |  |  |  |  |  | 3 | 3 | 
 |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 
 |  |  |  |  |  |  |  |  |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 0 | 

## Slide 21: Wavefront Pathplanning
BFS path planning
 | 15 |  |  |  |  |  |  |  |  |  | 
 | 14 | 14 |  |  |  |  |  |  | 6 |  | 
 | 13 | 13 |  |  |  |  |  |  | 5 | 5 | 
 | 12 | 12 |  |  |  |  |  |  | 4 | 4 | 
 | 12 | 11 |  |  |  |  |  |  | 3 | 3 | 
 |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 
 |  |  |  |  |  |  |  |  |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 0 | 

## Slide 22: Wavefront Pathplanning
BFS path planning
 | 15 |  |  |  |  |  |  |  |  |  | 
 | 14 | 14 |  |  |  |  |  |  | 6 |  | 
 | 13 | 13 |  |  |  |  |  |  | 5 | 5 | 
 | 12 | 12 |  |  |  |  |  |  | 4 | 4 | 
 | 12 | 11 |  |  |  |  |  |  | 3 | 3 | 
 |  | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 
 |  |  |  |  |  |  |  |  |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 0 | 

## Slide 23: Meadow Maps
A meadow map:

## Slide 24: Meadow Maps
A meadow map:
  Divides the map into convex polygons
  Interior of each polygon represents a “safe zone”
  Robot can move anywhere inside these polygons

## Slide 25: Meadow Maps
Place a vertex half way along every shared edge

## Slide 26: Meadow Maps
A meadow map, topological planning:

## Slide 27: Meadow Maps
A meadow map, topological planning:

## Slide 28: Generalised Voronoi Graph
Example

## Slide 29: Generalised Voronoi Graph
Divide space into Voronoi edges
These edges are equidistant from all points
Can be calculated on the fly
Can also be reasoned with (A*)
Wander when obstacles are out of range
Keep obstacles equidistant when in range

## Slide 30: Generalised Voronoi Graph
Navigation:

## Slide 31: Generalised Voronoi Graph
Navigation:

## Slide 32: Generalised Voronoi Graph
Navigation:

## Slide 33: Generalised Voronoi Graph
Navigation:
Obstacle detected

## Slide 34: Generalised Voronoi Graph
Navigation:
Two obstacles
detected

## Slide 35: Generalised Voronoi Graph
Navigation:
Two obstacles
detected
Follow the
Midpoint
This is the
Voronoi edge

## Slide 36: Generalised Voronoi Graph
Navigation:

## Slide 37: Generalised Voronoi Graph
Navigation:
Three obstacles
detected
Mark as node

## Slide 38: Generalised Voronoi Graph
Navigation:
Forms a navigable
graph

## Slide 39: Topological Maps
Detection of landmarks is the key
Think of driving instructions:
  Slight right at St Nicholas Circle 459 ft
  Keep left at the fork
  Continue to follow A47 0.1 mi
  Take the ramp onto Vaughan Way/A594 315 ft
  Slight left at Highcross St

## Slide 40: Topological Maps
Detection of landmarks is the key
Think of driving instructions:
  Slight right at St Nicholas Circle 459 ft
  Keep left at the fork
  Continue to follow A47 0.1 mi
  Take the ramp onto Vaughan Way/A594 315 ft
  Slight left at Highcross St
  Landmarks
  ...And instructions to navigate between them

## Slide 41: Topological Maps
Example getting from A to B
A
B

## Slide 42: Topological Maps
Example getting from A to B
A
B
Move forward beyond the doorway
Here

## Slide 43: Topological Maps
Example getting from A to B
A
B
Move forward until the wall directly in front is approximately 30cms away
Here

## Slide 44: Topological Maps
Example getting from A to B
A
B
Turn 90 counter clockwise
Here

## Slide 45: Topological Maps
Example getting from A to B
A
B
Move forward until the obstacle to the right is approx 90cm away and the left is approx 30cm away
Here

## Slide 46: Topological Maps
Example getting from A to B
A
B
Move forward until the obstacle to the right is approx 30cm away and increases to 90cm
Here

## Slide 47: (A Very Brief) Introduction to SLAM
Simultaneous Localization And Mapping
For details see Slam paper in LZ

## Slide 48: The Concept
Scene contains landmarks

## Slide 49: The Concept
Robot perceives landmarks

## Slide 50: The Concept
Robot moves – position estimated from odometry

## Slide 51: The Concept
Robot moves – position estimated from landmarks

## Slide 52: The Concept
Two possible positions – real position is in between

## Slide 53: The Concept
Two possible positions – real position is in between

## Slide 54: The SLAM Process

## Slide 55: Overview
Landmark extraction
  Map formed of discrete landmarks
  A different approach to occupancy grids
Data Association
  Have I seen this before?
  Attempt to match observed landmark to previously recorded landmarks
Extended Kalman Filter
  Form of Bayesian filter
  Uses covariance and rates of change – are landmarks moving together?

## Slide 56: Landmark Extraction
Method depends on sensors
Two main approaches:
  Outliers (spikes)
    Noise – will be eliminated by filter
    Spike features – table legs etc
  Inliers (RANSAC)
    Lines, shapes
    Corners make good landmarks

## Slide 57: Landmark Extraction
  Outliers (Spike Landmark Extraction )
    Noise – will be eliminated by filter
    Spike features – table legs etc

## Slide 58: Landmark Extraction
Method depends on sensors
  Inliers (RANSAC)
    Lines, shapes
    Corners make good landmarks

## Slide 59: Data Association
Nearest neighbour method
Extract landmarks
For each landmark
  Find closest landmark in landmark database
  Compare landmarks, if they match increment observation count, if not add landmark to database with one observation
Only consider landmarks observed at least N times

## Slide 60: EKF
Connects all parts of SLAM
Matrices hold
  Robot position
  Landmark positions
  Error
  Rates of change of all of these
  Gain to put everything together
Complex - see SLAM for Dummies for details
HILTI SLAM CHALLENGE 2022
  https://hilti-challenge.com/

## Slide 61: In Lab
Work on your second assignment.