## Slide 1: Lesson 7 – Particle Filters
Intelligent Mobile Robotics
Dr. Aboozar Taherkhani (PhD)
email: aboozar.taherkhani@dmu.ac.uk

## Slide 2: Overview
What is a particle filter?
Bayesian filters
Particle filters
Application to robot localization in 1dimension

## Slide 3: What is a Particle Filter?
In the real world we can’t trust single measurements
Knowledge about a measurement needs to be built up recursively over time given a series of measurements
We have already seen this with use of recursive Bayes’ to construct an occupancy grid

## Slide 4: What is a Particle Filter?
A particle is a single estimation of a quantity or vector of quantities
A particle filter uses a collection of particles to estimate the value of some quantity
The particles converge from a random initialization to a result given by a probability density function (PDF)
The PDF is discrete – made up of particles

## Slide 5: What is a Particle Filter?
A particle filter can be used for robot localization in a map

## Slide 6: What is a Particle Filter?
A particle filter is an implementation of a Bayesian filter
We’ll begin by looking at a Bayesian filter
Then see how particle filter realises an implementation of a Bayesian filter

## Slide 7: Bayes’ Filters
Bayes Filters address the problem of estimating the state x of a dynamical system from sensor measurements
Estimation given by a (posterior) PDF
Assumes at every time step t we have:
  A vector of control measurements ut
    Sensory perceptions about the system (ex. Robot Odometry)
  A vector of observations Zt
    Sensory perceptions about the environment (ex. Sonar reading)
  Both contain uncertainties

## Slide 8: Bayes’ Filtering
In general we want to estimate some vector x at time t so xt
The estimate is based on:
  The current observations
  A set of previous observations
  A set of previous control measurements
In the Fox paper this estimate is called Bel(xt)
For particle filters Bel(xt) is discrete
  Values of x with associated weights

## Slide 9: Bayes’ Filters
The posterior PDF at time t is denoted Bel(xt)
It is conditioned on all previous observations and control measurements
It is updated recursively in two phases:
  Prediction
    Use control measurements to estimate a new value of Bel(xt)
  Correction
    Use observations to assess new value of Bel(xt)

## Slide 10: Bayes’ Filters
Prediction
  Whenever a new measurement ut-1 is taken at time t
    NOTE: t-1 not t!
Correction
  Whenever an observation zt is taken at time t
Both are performed at time t

## Slide 11: Bayes’ Filters
Prediction
  Whenever a new measurement ut-1 is taken at time t
    NOTE: t-1 not t!
Correction
  Whenever an observation zt is taken at time t
Both are performed at time t
PDFs
Provide estimation of system state

## Slide 12: Bayes’ Filters
Prediction
  Whenever a new measurement ut-1 is taken at time t
    NOTE: t-1 not t!
Correction
  Whenever an observation zt is taken at time t
Both are performed at time t
Probabilistic model of system dynamics
Given state of system at t-1 and measurement of change in system, what is system like now?

## Slide 13: Bayes’ Filters
Prediction
  Whenever a new measurement ut-1 is taken at time t
    NOTE: t-1 not t!
Correction
  Whenever an observation zt is taken at time t
Both are performed at time t
Probabilistic model of perceptions
Given state, what is the likelihood of making this observation

## Slide 14: Bayes’ Filters
Prediction
  Whenever a new measurement ut-1 is taken at time t
    NOTE: t-1 not t!
Correction
  Whenever an observation zt is taken at time t
Both are performed at time t
Normalising factor
Ensure integral of Bel(xt) is 1

## Slide 15: Bayes’ Filters
Implementation
  To implement a Bayesian filter we need to implement three things:
    The belief probability density function:
    The model of system dynamics
    The perceptual model
In a particle filter these are all discrete functions

## Slide 16: Particle Filtering: Belief function
Belief function is a set S of n ordered pairs
Each ordered pair gives a single point in the belief function consisting of:
  A state:
  A weight (likelihood of that state):
  Overall:

## Slide 17: Particle Filtering: Model of system dynamics is probabilistic
  Lets assume system dynamics noise fits a normal distribution
  This distribution should be centred over the change in the system
  Standard deviation should be proportional to change in the system
  So:
      c = ut
      σ = k ut
      p(xt | xt-1, ut-1) = xt-1 + N(c, σ)
c
σ

## Slide 18: Particle Filtering
Perceptual Model is probabilistic:
  How to answer the question:
    “Given state x, what is the likelihood that I would make observation z?”
  We need an prior probabilistic model of the environment built through observation
  An occupancy grid will do nicely!

## Slide 19: Particle Filtering
Perceptual Model is probabilistic:
  State is (x, y, ) observation is (r, s)
  Likelihood of observation is: 1 – difference between contents of the grid square at (r, s) and actual observation

## Slide 20: Bayes’ Filters
Implementation
  To implement a Bayesian filter we need to implement three things:
    The belief probability density function:
    The model of system dynamics
    The perceptual model
In a particle filter these are all discrete functions
A set of ordered pairs
A sample from a normal
distribution based on the
movement of system
Prior discrete model of
observations




## Slide 21: Particle Filter Algorithm (Fox)

## Slide 22: 1D Robot Localisation Problem
A robot in a 1 dimensional world
  Can only go back or forward
  We’ll assume it only goes forward
  Lets run the particle filter algorithm!
Robot
Wall
Gaps in
the wall
1D occupancy
grid

## Slide 23: Particle Filter Algorithm (Fox)

## Slide 24: 1D Robot Localisation Problem
n = 100
Initialise St-1 with random numbers inside the dimensions of the wall, weighted to 1.0 / n
ut-1 = 0
zt-1 = 0
  St-1

## Slide 25: Particle Filter Algorithm (Fox)

## Slide 26: 1D Robot Localisation Problem
Select a value j in [1,n]
Selection needs to be weighted by particle weights
Use fitness proportionate selection (GAs)

## Slide 27: 1D Robot Localisation Problem
We know particle weights sum to one
Pick a random floating point number r in [0,1]
Set sum = 0
Iterate through particles i = 0..n doing
  sum += particle weight i
If (sum > r) stop, j = i

## Slide 28: Particle Filter Algorithm (Fox)

## Slide 29: 1D Robot Localisation Problem
Using our selected particle
Set values of c and σ based on ut-1
Sample dxt from N(c, σ)
xt = xt-1 + dxt

## Slide 30: Particle Filter Algorithm (Fox)

## Slide 31: 1D Robot Localisation Problem
wt = 1.0 – abs(particle perception – actual perception)
Particle perception
  Particle has a position in occupancy girid
  Particle’s perception is value in occupancy grid at x
Actual perception
  This needs to be simulated based on sensor reading
Add wt to 
Add to the set - does it have to be unique?

## Slide 32: Particle Filter Algorithm (Fox)

## Slide 33: 1D Robot Localisation Problem
Simple normalisation
Divide by 
Ensures integral of St is 1

## Slide 34: 1D Robot Localisation Problem
Final step:
  Estimate the state
  Use mean of maximum
  Let the maximum value of wt be M
  Let xm be the set of particle states with a weight of M
    {xi | wi = M, i=1..n}
  Estimated state =  xi
  #xm

## Slide 35: 1D Robot Localisation Problem
Particle filter in action t=0

## Slide 36: 1D Robot Localisation Problem
Particle filter in action t=1

## Slide 37: 1D Robot Localisation Problem
Particle filter in action t=2

## Slide 38: 1D Robot Localisation Problem
Particle filter in action t=3

## Slide 39: 1D Robot Localisation Problem
Particle filter in action t=9

## Slide 40: 1D Robot Localisation Problem
Particle filter in action t=10

## Slide 41: 1D Robot Localisation Problem
Particle filter in action t=11

## Slide 42: 1D Robot Localisation Problem
Particle filter in action t=12

## Slide 43: 1D Robot Localisation Problem
Particle filter in action t=13

## Slide 44: 1D Robot Localisation Problem
Particle filter in action t=21

## Slide 45: 1D Robot Localisation Problem
Particle filter in action t=22

## Slide 46: 1D Robot Localisation Problem
Particle filter in action t=23

## Slide 47: 1D Robot Localisation Problem
Real time demo
  Don’t expect it to work every time

## Slide 48: Summary
Bayes’ filters apply recursive Bayes’ to a chain of motions and observations to estimate a state vector
Particle filters implement Bayes’ filters with sampled probability, so discrete PDFs
Particle filters can be used for localization
Demonstrated how to perform 1D localization